## Slide 1
■再防活動推進体制図
防災活動責任者
総合受付
承認者
担当
確認者
1. 再防活動の体制
HMSI
Musashi Auto Parts India (以下 MAP-ID)
〇 | 澤村 良信
所属 : HMSI 役職 : 品質管理責任者 所属 : HMSI 役職 : 品質管理責任者 | 
〇 | ガウラブ・アガルワル
所属: HMSI 役職: 工場CIQ 所属: HMSI 役職: 工場CIQ | 
〇 | アミット・ダワール
所属 : HMSI QC 役職 : 総支配人 所属 : HMSI QC 役職 : 総支配人 | 
〇 | ヴィジャイ・トリパーティ ラヴィランジャン ヴィジャイ・トリパーティ ラヴィランジャン
所属部門: HMSI 品質管理 役職: 部長 所属部門: HMSI 品質管理 役職: 部長 | 
〇 | アニル・ゴギア 鹿所 道弘 アニル・ゴギア 鹿所 道弘
所属 : HMSI QC 役職 : 総支配人 / コーディネーター 所属 : HMSI QC 役職 : 総支配人 / コーディネーター | 
〇 | カシャップ・ヴァイバヴ
所属 : HMSI QC 役職 : 部長 所属 : HMSI QC 役職 : 部長 | 
〇 | 白井 智也
所属 : MAP-ID 役職 : 代表取締役 所属 : MAP-ID 役職 : 代表取締役 | 
〇 | 鈴木 勝久
所属 : QE 役職 : 副部長 所属 : QE 役職 : 副部長 | 
〇 | パルヴィーン・マーン ナレシュ・パル パルヴィーン・マーン ナレシュ・パル
所属部門: 品質保証/生産 役職: 副部長/シニア部長 所属部門: 品質保証/生産 役職: 副部長/シニア部長 | 
〇 | アショック・クマール サンディープ・クマール アショック・クマール サンディープ・クマール
所属 : QE / 生産 役職 : マネージャー / シニアマネージャー 所属 : QE / 生産 役職 : マネージャー / シニアマネージャー | 
防災活動責任者
承認者
担当
確認者
No changes since the second interim verification meeting

## Slide 2
CBF150 | CBF125
CB350 | MC300
 | モデル | カムフランジ角度 | フランジ | ベアリング | 外観 | 検査頻度
1 | CBF150 | 159°17’ | 同部品 | 同部品 | 類似 | 全数検査
2 | CBF125 | 160°47’ |  |  |  | 
3 | SCV110 | 117°06’ | 同部品 | 同部品 | 類似 | 
4 | SCV125 | 118°33’ |  |  |  | 
5 | CBF160 | 159°46’ | 同部品 | 同部品 | 類似 | 
6 | CBF190 | 161°01’ |  |  |  | 
COMモデル（従来）
FUNモデル（今回）
2. 概要 (変化点)
COMモデルは混入観点で全数検査を実施していたため、不具合品の流出は無い
■設備使用の経緯
外観で区別がつかないカムシャフトを生産している
↓
混入観点で全数検査を実施
フランジ
ベアリング
ベアリング
カムシャフト
フランジ
ベアリング
カムシャフト
ベアリング
専用部品を使用しており外観で区別が可能
↓
抜取検査を実施
フランジ
ベアリング
カムシャフト
ベアリング
ベアリング
カムシャフト
フランジ
ベアリング
部品、形状が相違
部品、形状が類似
■当該設備で生産しているカムシャフトの違い
設備導入
2014年
COMモデル生産
FUNモデル生産
（FUN専用設備として使用）
2017年～2020年
2020年～
 | モデル | カムフランジ角度 | フランジ | ベアリング | 外観 | 検査頻度
1 | CB350 | 121°09’ | 専用品 | 専用品 | 相違 | 抜取検査
2 | MC300 | 116°50’ | 専用品 | 専用品 | 相違 | 
No changes since the second interim verification meeting

## Slide 3
Non-compliance with procedures: The operator adjusted the angle adjustment pin without supervisor approval
Root Cause: Operator made adjustments that impacted product accuracy
(Rule: Adjustments are to be performed by Line Leader)
The camshaft retention condition was poor after flange insertion, resulting in camshaft collapse
(Loosening of the retention due to wear of the ball plunger)
As the camshaft tilt issue remained unresolved, the operator escalated to the line leader
The line leader adjusted the ball plunger in the bearing seat, resolving the issue of product tipping.
Cause of Leakage... Appropriate Traceability Inspection (Previous Production Lot) Was Not Conducted
Non-conforming products were not identified
(Rule: In Case of Abnormality, All Work-in-Progress and Inventory Shall Be Held for Inspection)
The operator did not report the angle adjustment pin adjustment to the line leader.
The flange insertion angle issue was not detected, and production continued.
(Rule: If an abnormality occurs, the operator must stop processing and report it to the supervisor.)
発生
15日流出
②
1.
Production resumed 14 days later, and [a camshaft flange press-fit issue was detected during setup evaluation]. However, non-conforming products were not identified, and proper traceability sorting was not conducted, resulting in the release of non-conforming products
(Rule: If the equipment has been idle for 4 consecutive days or more, the setup approval rule shall be applied)
Contributing Factors - The adjustment mechanism lacked covers, allowing for easy adjustment
②
① Change Point:
② Cause:
Instead of adjusting the ball plunger in the bearing housing,
the angle adjustment pin was adjusted
ball plunger in the bearing housing
↓
Retain Camshaft
Angle Adjustment Bolt
↓
Flange Insertion Angle Adjustment
Occurrence: The operator made adjustments that affected product accuracy
Sr. No | [Input/Open] | [Input/Close] | [Output/Open] | [Output/Close]
 | -10° ± 3° | 26° (± 3°) | 30° (± 3°) | -3° ± 3°
1 | -30° | 47° | 9° | 16°
2 | -28° | 46° | 11° | 13 degrees
3 | -29° | 48° | 8 degrees | 16°
During the sampling inspection, a camshaft flange press-fit issue was
identified.
Incident:
Rear of Angle Adjustment Pin
Angle Adjustment Pin
29日流出
HMSI assembles and inspects defective products from clients, then ships them directly
* Discovered valve timing misalignment during monthly random inspections
Due to valve timing misalignment, the exhaust gas (CO) value exceeds the standard, resulting in non-compliance with regulations.
Top View
Front View
Actual line
Center line
Actual line
Center line
Flange
Flange shifted with respect to Keyway
Leakage: Appropriate retrospective screening was not conducted (screening rules were ambiguously expressed)
Non-conforming products were not identified
3. Mechanism of Occurrence
No changes since the second interim verification meeting
Notes: ＊起点となる要因から最終事象までを順を追って文章で記載する。用語は一般的なもの（たとえばJISやJASO用語）を用い、
本田用語は極力使わない。